TECHNICAL DATA SHEET

STEREO SPEAKER TWIN CABLES

AM Part No’s:- 550 - 555

Profile:

Twin flat figure of 8, suitable for wiring speaker systems in vehicles and in the home.

Insulation Properties:

PVC insulation compound to BS6746 Type TI1

Operating temperature.	-15(C to 70(C

Plain copper wires conforming to BS6360

Copper Properties & Cable Dimensions

Part No.	Copper	Cross		Current	Overall	    Sheath-

Section	Rating	    Dia		    Core colours

(mm)		 (amps)		   (mm)

550		2 x 12/0.2            2 x 0.38	                  2.0		 3.6 x 1.7        Black - Black/White

551		2 x 16/0.2	 2 x 0.50	                  3.0		 3.9 x 1.9        Black - Black/White

552		2 x 24/0.2	 2 x 0.75	                  6.0		 4.3 x 2.1        Black - Black/Red

553		2 x 32/0.2	 2 x 1.0		  10.0		 4.6 x 2.3        Black - Black/Blue

554		2 x 30/0.25	 2 x 1.5		  15.0		 5.9 x 2.8        Trans -Trans/Green

555		2 x 50/0.25	 2 x 2.5  	                20.0		 7.3 x 3.5        Trans -Trans/ Yellow